## Slide 1
Detection and Prevention of
Spoofing Attacks in the
Internet of Underwater Things
A Comparative Review of Learning-Based Physical-Layer Authentication Techniques
Sehrish Siddique and Tatheer Zahra
Introduction to Information Security
Semester Research Project
Comparative Review
Ten representative PLA studies
IoUT Security
Spoofing + impersonation
PLA-Based Defense
Channel evidence for trust
🛡
Acoustic fingerprint ≠ copied identity
Notes: Presenter 1 opens by introducing the topic as an information security research review focused on underwater networks. Explain that this presentation does not propose a new spoofing detection algorithm. It reviews and compares ten representative physical-layer authentication studies. Emphasize the key idea: underwater nodes may be logically impersonated, but their acoustic channel behavior can provide evidence of their physical origin. The deck moves step by step from IoUT basics to spoofing attacks, PLA, method families, comparison, challenges, recommendations, and social usefulness.

## Slide 2
IoUT Spoofing Defense | PLA Comparative Review
2
Why This Topic Matters
Security failure affects trust in underwater decisions
🌊
Marine
monitoring
⚠
Disaster
warning
⚙
Offshore
infrastructure
🛡
Security
trust
Why spoofing matters
IoUT supports marine monitoring, disaster warning, offshore infrastructure, surveillance, and underwater data collection.
Security failures can damage trust in monitoring and decision-making.
Spoofed data may be accepted as legitimate if authentication fails.
Underwater security affects both technical reliability and real-world safety.
Supported by: Aman et al. [9] — LoS impersonation detection; Xiao et al. [4] — RL/DRL learning-based PHY-layer authentication
Notes: This slide explains why the topic matters beyond theory. IoUT systems can support environmental observation, disaster-warning systems, underwater surveillance, and infrastructure monitoring. If a malicious node injects false data, the system may make decisions using incorrect information. That means spoofing is not just a network attack; it can affect monitoring accuracy, trust, and operational safety. The main motivation of the paper is to understand how physical-layer authentication can help detect and reject such false transmissions in the difficult underwater environment.

## Slide 3
IoUT Spoofing Defense | PLA Comparative Review
3
What is IoUT?
Underwater sensors, mobile devices, surface sinks, and monitoring stations
Definition
IoUT extends networked sensing and communication into underwater environments.
Sensors collect physical or environmental data.
AUVs/mobile nodes inspect, relay, or collect data.
Surface sinks forward data to remote monitoring systems.
●
Underwater
Sensors
▰
AUVs /
Mobile Nodes
▲
Surface
Sink
▣
Monitoring
Station
Typical data flow: underwater observation → acoustic link → surface forwarding → remote/base/cloud monitoring
Notes: IoUT can be explained as the underwater version of networked sensing and communication. The basic architecture includes underwater sensors, mobile devices such as AUVs, surface sinks, and monitoring stations. Data normally starts at underwater sensors, travels through acoustic links, reaches a surface sink, and then moves to a terrestrial or cloud-based monitoring system. This architecture creates many useful applications, but it also creates a difficult authentication problem because the communication channel is underwater, mobile, noisy, and resource-constrained.

## Slide 4
IoUT Spoofing Defense | PLA Comparative Review
4
Why IoUT Security is Different from Normal IoT
Acoustic communication changes the security design problem
Terrestrial IoT
Mostly RF communication
Lower propagation delay
More bandwidth in many deployments
Easier physical access for maintenance
IoUT
Mainly acoustic communication
Limited bandwidth + long propagation delay
Multipath, Doppler effects, and high bit-error rate
Mobile and energy-constrained nodes
Design implication: authentication must be secure without excessive retransmission, delay, computation, or packet overhead.
Context from: Zhao et al. [1] — PLA without adversary training data; Ardizzon et al. [5] — RNN/LSTM mobile PLA; Casari et al. [10] — Mobility-aware PLA with mobile devices
Notes: Normal IoT security assumptions do not transfer directly to underwater networks. In water, RF signals attenuate quickly, so acoustic communication is commonly used. Acoustic links are slow, narrow-band, noisy, and affected by multipath and Doppler effects. Many underwater nodes also run on batteries that are difficult to replace. This means long handshakes, frequent retransmissions, and heavy cryptographic exchanges can become expensive. The paper argues that IoUT authentication must respect both security goals and underwater communication constraints.

## Slide 5
IoUT Spoofing Defense | PLA Comparative Review
5
Spoofing and Impersonation Attack Model
Logical identity may not match physical origin
Attack behavior
Malicious transmitter pretends to be a legitimate underwater node.
It may forge identity, send fake readings, or transmit misleading control messages.
Receiver may accept false data if authentication fails.
Impact: corrupted monitoring, routing confusion, wasted bandwidth, reduced trust.
Legitimate
Sensor
Attacker
Node
Receiver /
Sink
Claimed ID: Sensor A
Aman et al. [9] — LoS impersonation detection; Xiao et al. [4] — RL/DRL learning-based PHY-layer authentication
Notes: Spoofing in IoUT is an identity-deception attack. A malicious transmitter may use a legitimate node identifier or imitate its packet format. If the receiver trusts that packet, false data can enter the monitoring or routing process. The paper treats spoofing and impersonation as closely related because both involve a mismatch between the claimed logical identity and the real physical origin of the signal. This mismatch is the opportunity that physical-layer authentication tries to detect using channel evidence.

## Slide 6
IoUT Spoofing Defense | PLA Comparative Review
6
Why Spoofing is Hard in IoUT
The legitimate channel also changes naturally
Hard constraints
Nodes are remote and hard to physically monitor.
Heavy authentication handshakes consume bandwidth and energy.
Channels change due to movement and environment.
A moving legitimate node may look suspicious if the method is not mobility-aware.
AUV at t1
AUV at t2
Fingerprint changes ≠ always attack
Mobility-focused sources: Ardizzon et al. [5] — RNN/LSTM mobile PLA; Ventura et al. [6] — Location-tracking authentication; Casari et al. [10] — Mobility-aware PLA
Notes: Spoofing defense is hard because the underwater channel itself is unstable. A legitimate sensor or AUV may move, the water environment may change, and the multipath structure may vary over time. If authentication relies on a fixed channel fingerprint, a real node may be falsely rejected. At the same time, underwater nodes cannot afford repeated retransmissions or expensive authentication traffic. This creates the central challenge: the defense must detect spoofing while avoiding false alarms caused by normal underwater dynamics.

## Slide 7
IoUT Spoofing Defense | PLA Comparative Review
7
Review Aim, Research Questions, and Contribution
A focused comparative review - not a new algorithm or experimental implementation
Research Questions
RQ1: Which physical-layer features are most commonly used for spoofing and impersonation detection in IoUT-related underwater acoustic networks?
RQ2: How do learning-based PLA techniques differ in adaptability, energy cost, computational complexity, and mobility support?
RQ3: Which methods rely on adversary training data, historical CIR databases, cooperative nodes, localization models, or real-environment validation?
RQ4: What practical research gaps still prevent deployment of PLA-based spoofing defense in real IoUT systems?
Review Contribution
Organizes ten representative IoUT-related spoofing and PLA studies by feature source, learning mechanism, and authentication decision.
Compares methods by attack model, PLA feature, decision method, mobility support, adversary-data requirement, evaluation basis, strengths, and limitations.
Identifies research gaps and future directions for practical IoUT spoofing defense.
Emphasizes lightweight, adaptive, mobility-aware, explainable, benchmarked, and hybrid PLA frameworks.
Problem
Research Questions
Comparative Review
Gaps / Future Directions
Notes: This slide clarifies the academic aim of the work. The paper is not proposing a new model, algorithm, dataset, or experimental implementation. Instead, it reviews ten representative studies to answer four research questions. These questions guide the full presentation: which physical-layer features are used, how learning-based PLA methods differ, which practical assumptions each method depends on, and what gaps still block real deployment. The contribution is the structured comparison, taxonomy, and research direction for practical IoUT spoofing defense.

## Slide 8
IoUT Spoofing Defense | PLA Comparative Review
8
Core Defense Idea: Physical-Layer Authentication
Identity can be copied, but channel fingerprints are difficult to reproduce
PLA principle
Authenticates a transmitter using physical evidence from the communication link.
A node ID or packet format can be copied.
The exact acoustic channel fingerprint is difficult to reproduce.
PLA complements higher-layer security; it is not a total replacement.
Claimed ID
Node A
Physical Evidence
CIR • PDP • delay • location • TR • history
Authentication decision
Does the physical evidence match the claimed identity?
Evidence examples: CIR, PDP, arrival delay, statistical channel parameters, location consistency, time-reversal response, historical fingerprints.
Examples from: Zhao et al. [1] — PLA without adversary training data; Shi et al. [2] — Database-based PLA; Xiao et al. [4] — RL/DRL adaptive PLA; Zhao et al. [8] — Time-reversal PLA
Notes: Physical-layer authentication uses the communication link itself as an authentication source. A malicious node can copy a packet ID, but it cannot easily recreate the exact acoustic path between a legitimate transmitter and receiver. The receiver can therefore compare claimed identity with physical evidence such as CIR, PDP, delay behavior, time-reversal response, or location consistency. The key point is that PLA works as a complementary defense. It improves identity verification, but it still has practical limits such as channel drift, training needs, and deployment assumptions.

## Slide 9
IoUT Spoofing Defense | PLA Comparative Review
9
PLA Pipeline for Spoofing Defense
How detection becomes authentication-based rejection
1
Signal
reception
Packet or acoustic observation
2
Feature
extraction
CIR, PDP, delay, location, TR, history
3
Decision
processing
Compare, classify, predict, or fuse
4
Authentication
decision
Legitimate, suspicious, or unauthenticated
5
Security
action
Accept, reject, flag, isolate, ignore, re-authenticate
Prevention in this review means operational non-acceptance after failed authentication - not physically stopping transmission.
Pipeline summarized across the ten reviewed PLA studies in the uploaded paper.
Notes: The paper describes PLA as a pipeline. First, the receiver obtains a packet or acoustic observation. Second, it extracts channel-dependent features such as CIR, PDP, arrival delay, location estimates, or historical fingerprint differences. Third, a decision method compares, classifies, predicts, or fuses the evidence. Fourth, the packet or node is marked legitimate, suspicious, or unauthenticated. Finally, the security action happens: accept, reject, flag, isolate, ignore, or ask for re-authentication. This is how detection becomes operational prevention.

## Slide 10
IoUT Spoofing Defense | PLA Comparative Review
10
Learning-Based PLA Methods Reviewed
A method-family map of the ten representative studies
Learning-Based
PLA for IoUT
Spoofing Defense
RL / DRL
Xiao et al. [4] — adaptive thresholds
SVM
Zhao et al. [1] — no adversary training data
RNN / LSTM
Ardizzon et al. [5] — mobile feature prediction
CNN / Location
Ventura et al. [6] — trajectory consistency
Cooperative
Diamant et al. [7] — trusted-node fusion
TR / Database / CIR
Zhao et al. [8], Shi et al. [2], Zhao et al. [3]
Notes: This slide gives the audience the map of the reviewed literature. The ten studies are not all solving the same subproblem. Some learn adaptive thresholds, some classify channel fingerprints, some predict mobile channel evolution, some use location consistency, and others fuse evidence from trusted nodes. Time-reversal and historical CIR methods use multipath and stored channel behavior as security evidence. The purpose of the review is to compare these families carefully rather than claim that one method is universally best.

## Slide 11
IoUT Spoofing Defense | PLA Comparative Review
11
RL/DRL and SVM-Based Authentication
Adaptive learning versus classifier-based PLA
Xiao et al. [4] — RL/DRL adaptive PLA
Uses PDP-based physical evidence.
Learns or adapts authentication parameters and thresholds.
Useful under uncertainty and channel variation.
Deployment limitation: higher training and computational cost.
Zhao et al. [1] — PLA without adversary training data
Uses CIR/database-correlative features.
Important when real adversary samples are unavailable.
Fits resource-constrained underwater settings better than heavier methods.
Deployment limitation: relies on representative legitimate CIR records.
Notes: RL and DRL authentication are useful when the correct threshold is uncertain. Xiao et al. use PDP evidence and adjust authentication decisions through learning. This helps in dynamic settings but may increase computation and training cost. The SVM-based direction in Zhao et al. addresses a different practical issue: real attacker data may be difficult to collect underwater. It uses CIR-related features and avoids requiring real adversary training samples. This makes it attractive for resource-constrained networks, although the legitimate channel database still has to remain useful.

## Slide 12
IoUT Spoofing Defense | PLA Comparative Review
12
Mobility-Aware Authentication
Avoid false alarms caused by legitimate node movement
Core problem
Mobile nodes and AUVs naturally change channel fingerprints.
A static fingerprint can reject a legitimate moving node.
Authentication must track expected change, not only current mismatch.
Reviewed directions
Ardizzon et al. [5] — RNN/LSTM mobile PLA; Ventura et al. [6] — Location-tracking authentication; Casari et al. [10] — Mobility-aware PLA with mobile devices.
Predicted path
Suspicious deviation
Notes: Presenter 2 can begin here by explaining that mobility is one of the biggest differences between underwater authentication and simple static fingerprinting. AUVs, drifting nodes, and mobile relays naturally change their channel behavior. If a method assumes the channel is fixed, it may reject a valid mobile node. RNN/LSTM methods predict the evolution of channel features, while location-tracking approaches estimate and predict a node path. The common goal is to treat legitimate movement as expected behavior while still detecting abnormal deviations.

## Slide 13
IoUT Spoofing Defense | PLA Comparative Review
13
Cooperative, Time-Reversal, and Historical CIR Methods
Using spatial diversity, multipath, and channel history as security evidence
Diamant et al. [7] — Cooperative authentication
Trusted helper nodes evaluate local beliefs.
Sink fuses multiple decisions.
Spatial diversity makes spoofing harder across receivers.
Deployment concern: trusted helpers and extra overhead.
Zhao et al. [8] — Time-reversal PLA
Uses MTRRS and multipath focusing as a link signature.
Turns multipath from impairment into security evidence.
Deployment concern: depends on CIR/time-reversal estimation.
Shi et al. [2] / Zhao et al. [3] — Database and differential CIR PLA
Compares current channel evidence with historical CIR/link fingerprints.
Handles dynamic channels.
Deployment concern: records must stay updated.
Notes: These methods use physical diversity and channel history. Cooperative authentication uses trusted nodes so that the sink does not depend on one receiver only. Time-reversal authentication uses multipath focusing behavior as a link signature, which is interesting because multipath becomes useful security evidence instead of only a communication problem. Database-based and differential CIR methods compare present channel observations with historical link fingerprints. They are suitable for dynamic channels, but they introduce database aging, update, and storage challenges.

## Slide 14
IoUT Spoofing Defense | PLA Comparative Review
14
Literature Synthesis: How the 10 Papers Fit Together
Six research directions, not ten isolated summaries
1
Statistical / hypothesis-testing
impersonation detection
Aman et al. [9] — LoS impersonation detection
2
Adaptive learning-based
authentication
Xiao et al. [4] — RL/DRL adaptive PLA
3
Adversary-data-free
PLA
Zhao et al. [1] — PLA without adversary training data
4
Mobility-aware
authentication
Casari et al. [10]; Ardizzon et al. [5]; Ventura et al. [6]
5
Cooperative
authentication
Diamant et al. [7] — Cooperative authentication
6
Time-reversal / database /
differential CIR authentication
Zhao et al. [8]; Shi et al. [2]; Zhao et al. [3]
Notes: This slide synthesizes the literature instead of listing papers one by one. The review groups the studies into six research directions. Aman et al. provide an underwater impersonation baseline using hypothesis testing. Xiao et al. focus on learning adaptive authentication parameters. Zhao et al. address adversary-data scarcity. Casari, Ardizzon, and Ventura handle mobility and location consistency. Diamant et al. use cooperative verification. Other Zhao and Shi works use time-reversal, database, and differential CIR logic. This grouping makes the review more viva-defensible.

## Slide 15
IoUT Spoofing Defense | PLA Comparative Review
15
Comparative Analysis: What Was Compared?
The paper compares method assumptions, evidence, and deployment conditions
Technical View
Attack model
PLA feature
Decision method
Deployment View
Adversary-data requirement
Mobility support
Evaluation type
Practical View
Main strength
Main limitation
Deployment assumption
Examples used in the comparison: Aman et al. [9] — LoS impersonation detection; Xiao et al. [4] — RL/DRL adaptive authentication; Zhao et al. [1] — No adversary training data; Diamant et al. [7] — Cooperative authentication
The reviewed studies use different models, features, metrics, and validation settings; therefore, direct numerical ranking would be misleading.
Notes: This slide explains the comparison dimensions used in the review. The paper does not copy results into a direct accuracy ranking, because the studies use different models, physical features, metrics, and validation settings. Instead, the review compares three types of evidence. The technical view covers attack model, PLA feature, and decision method. The deployment view covers adversary data, mobility support, and evaluation type. The practical view covers strength, limitation, and deployment assumption. This makes the comparison fairer and more academically defensible.

## Slide 16
IoUT Spoofing Defense | PLA Comparative Review
16
Qualitative Comparison of PLA Method Families
Qualitative comparison only - methods are not directly ranked by accuracy
Method Family
Adaptability
Energy / Computation
Mobility
Deployment Concern
RL/DRL-based PLA
Xiao et al. [4] — RL/DRL PHY-layer authentication
High
High
Medium
Adaptive but computationally demanding
SVM without adversary data
Zhao et al. [1] — PLA without adversary training data
Medium
Low–Medium
Low–Medium
Practical when adversary samples are unavailable; depends on reliable CIR records
RNN/LSTM mobile PLA
Ardizzon et al. [5] — RNN/LSTM mobile PLA
High
High
High
Strong for mobility but needs training and tuning
CNN/location tracking
Ventura et al. [6] — Location-tracking authentication
High
High
High
Promising for mobility but localization-dependent
Cooperative authentication
Diamant et al. [7] — Cooperative authentication
Medium
Medium–High
Medium
Useful where trusted helper nodes are available
Time-reversal PLA
Zhao et al. [8] — Time-reversal PLA
Medium
Medium
Low–Medium
Physically grounded but depends on CIR/time-reversal estimation
Database/differential CIR PLA
Shi et al. [2] — Database-based PLA; Zhao et al. [3] — Differential CIR feature-based PLA
High
Medium
Medium
Suitable for dynamic channels but needs database maintenance
Qualitative comparison only — methods are not directly ranked by accuracy because evaluation settings differ.
Notes: This slide is a qualitative comparison, not a direct accuracy ranking. The reviewed studies use different channel models, attack assumptions, datasets, metrics, and validation settings, so ranking them numerically would be misleading. The table compares method families using adaptability, energy or computation cost, mobility support, and deployment concern. RL and deep learning methods are adaptive but heavier. SVM is practical when attacker samples are unavailable. Mobility-aware methods are strong for moving nodes. Cooperative, time-reversal, database, and differential CIR methods are useful, but each depends on specific deployment assumptions.

## Slide 17
IoUT Spoofing Defense | PLA Comparative Review
17
Taxonomy of Reviewed Techniques
A multidimensional view avoids forcing overlapping methods into one category
1. Physical-layer feature source
CIR / PDP
Location / AoA / delay
Time-reversal response
Historical / differential CIR
2. Decision mechanism
Hypothesis testing / ML estimation
RL / DRL
SVM / classification
RNN / LSTM prediction
CNN localization
Cooperative belief fusion
3. Deployment condition
Resource-constrained nodes
Mobile nodes
Dynamic channels
Multi-receiver cooperative settings
Mapped across: Zhao et al. [1], Shi et al. [2], Zhao et al. [3], Xiao et al. [4], Ardizzon et al. [5], Ventura et al. [6], Diamant et al. [7], Zhao et al. [8], Aman et al. [9], Casari et al. [10]
Notes: The taxonomy is multidimensional because one method can belong to more than one category. For example, a method may use CIR as a physical feature but SVM as its decision mechanism. Another may use location behavior with CNN localization and mobility prediction. The taxonomy separates feature source, decision mechanism, and deployment condition. This helps the audience understand that PLA is not one single technique. It is a family of authentication designs built around different channel evidence and different operational assumptions.

## Slide 18
IoUT Spoofing Defense | PLA Comparative Review
18
Challenges and Limitations
PLA is promising, but deployment readiness still depends on several constraints
Benchmarks
Limited common datasets + heterogeneous evaluation
Mobility
False alarms from legitimate movement
Trade-off
False acceptance vs false rejection
Adversary data
Realistic attack samples are scarce
Overhead
Energy, computation, memory, communication cost
Assumptions
Database aging, channel drift, trusted nodes, localization, scalability
These limitations appear across the reviewed studies and explain why no single PLA method dominates all IoUT deployments.
Notes: The paper emphasizes that PLA is promising, but not deployment-ready in every setting. There are few common benchmarks, so fair comparison is difficult. Mobility can make legitimate nodes look suspicious. False acceptance and false rejection must be balanced carefully because retransmission is costly underwater. Real attacker data is scarce, and deep learning or cooperative methods may increase computation and communication overhead. Historical databases can age, localization may be inaccurate, and trusted helper nodes may not always exist. These challenges explain why no method dominates all scenarios.

## Slide 19
IoUT Spoofing Defense | PLA Comparative Review
19
Recommendations and Future Research Directions
Toward lightweight, adaptive, benchmarked, explainable, and hybrid defense
Recommendations
Use lightweight and energy-aware authentication models.
Use adaptive thresholds and channel-history-aware PLA.
Design mobility-aware prediction and trajectory-consistency checks.
Prefer adversary-data-free approaches when attacker samples are unavailable.
Improve benchmarking and evaluation fairness.
Combine PLA with lightweight cryptography where feasible.
Add explainable authentication decisions.
Future research directions
Benchmark datasets and reproducibility.
Online/adaptive learning without normalizing attacker behavior.
Cross-environment transfer learning.
Federated/distributed learning as a future direction, not a proven result.
Mobility-aware hybrid authentication.
Energy-aware model compression.
Robustness against model drift, poisoning, and adaptive spoofers.
Main takeaway: Practical spoofing defense should be lightweight, adaptive, mobility-aware, explainable, benchmarked, and hybrid.
Notes: This merged slide connects recommendations with future research. The recommendations follow directly from the identified gaps: lightweight models for energy limits, adaptive thresholds for dynamic channels, mobility-aware prediction for AUVs and drifting nodes, adversary-data-free approaches when attacker samples are unavailable, and better benchmarking for fair comparison. Future work should also study online learning carefully, because models must adapt without learning attacker behavior as normal. Transfer learning, federated learning, hybrid authentication, model compression, robustness, and explainability are important directions, but they should be treated as future directions rather than already proven deployment results.

## Slide 20
IoUT Spoofing Defense | PLA Comparative Review
20
How This Research is Useful for Students and Society
Final main content slide
For students
Understand IoT security beyond normal terrestrial networks.
Connect information security, machine learning, signal processing, and networking.
Learn how to critically compare research papers.
Build awareness of real deployment constraints: energy, delay, mobility, and scalability.
For society
Support safer marine monitoring and disaster-warning systems.
Help protect underwater infrastructure and environmental sensing.
Reduce risk of false data entering underwater decision systems.
Encourage secure and sustainable underwater technology.
“Securing underwater networks means protecting the trustworthiness of future ocean monitoring, exploration, and safety systems.”
Notes: This final content slide connects the research to learning and social value. For students, the paper is useful because it shows how information security changes when the network environment changes. It connects security, machine learning, signal processing, and networking. It also teaches how to compare research honestly without overstating results. For society, secure IoUT can support safer monitoring, disaster warning, environmental sensing, and underwater infrastructure protection. The closing message is that securing underwater communication protects the trustworthiness of future ocean systems.

## Slide 21
IoUT Spoofing Defense | PLA Comparative Review
21
Appendix — References
Reviewed studies from the uploaded paper
Compact citation key
Zhao et al. [1] — PLA without adversary training data; IEEE Sensors Journal, 2023.
Shi et al. [2] — Database-based PLA for dynamic underwater acoustic networks; OCEANS 2023.
Zhao et al. [3] — Differential CIR feature-based PLA; IEEE Sensors Journal, 2025.
Xiao et al. [4] — RL/DRL learning-based PHY-layer authentication; IEEE Communications Letters, 2019.
Ardizzon et al. [5] — RNN/LSTM mobile PLA; Computer Networks, 2024.
Ventura et al. [6] — Location-tracking authentication; arXiv preprint, 2024.
Diamant et al. [7] — Cooperative authentication; IEEE Transactions on Wireless Communications, 2019.
Zhao et al. [8] — Time-reversal PLA; IEEE Sensors Journal, 2022.
Aman et al. [9] — LoS impersonation detection; IEEE Access, 2018.
Casari et al. [10] — Mobility-aware PLA with mobile devices; WUWNet, 2022.
Use this slide only as backup for viva questions; the main presentation ends on Slide 20.
Notes: This appendix is included for academic completeness and should not be treated as part of the main 20-minute content. It helps the presenters answer viva questions about where each method family came from. Keep the slide compact and avoid reading every reference aloud. Instead, use it as a backup if the instructor asks which papers support a specific method. The main presentation should end clearly on Slide 20, and this reference key should remain available afterward.